## Slide 1: Fuzzy Logic Block Diagram

## Slide 3
Functional Blocks of FIS
The following five functional blocks will help you understand the construction of FIS −
Rule Base − It contains fuzzy IF-THEN rules.
Database − It defines the membership functions of fuzzy sets used in fuzzy rules.
Decision-making Unit − It performs operation on rules.
Fuzzification Interface Unit − It converts the crisp quantities into fuzzy quantities.
Defuzzification Interface Unit − It converts the fuzzy quantities into crisp quantities. Following is a block diagram of fuzzy interference system.

## Slide 4: Fuzzy ruled based system (or) interference Engine
In rule-based fuzzy systems, the relationships between variables are represented by means of fuzzy if–then rules of the following general form:
If antecedent proposition( A set of conditions satisfy ) then consequent proposition( A set of consequent)
The antecedent proposition is always a fuzzy proposition of the type
“~ x is A”
Where
~x is a linguistic variable and
A is a linguistic constant (term).

## Slide 5
A collection of rules refering to a particular system is known as fuzzy rule base.
If the conclusion C to be drawn from the rule base R is the conjunction of all the individual Consequents Ci of each rule then
C=C1UC2U......... Cn
µC(y)= Max (µC1(y), µC2(y).......... µCn(y))
Similarly for intersection we should consider
µC(y)= Min (µC1(y), µC2(y).......... µCn(y))

## Slide 6: Graphical Representation of Fuzzy
As a general example, consider the design of a fuzzy controller for a steam turbine.
The block diagram of this control system appears as follows:
The input and output variables map into the following fuzzy set:

## Slide 8
The rule set includes such rules as
rule 1: IF temperature IS cool AND pressure IS weak, THEN throttle is P3.
rule 2: IF temperature IS cool AND pressure IS low, THEN throttle is P2.
rule 3: IF temperature IS cool AND pressure IS ok, THEN throttle is Z.
rule 4: IF temperature IS cool AND pressure IS strong, THEN throttle is N2.

## Slide 9
For an example, assume the temperature is in the "cool" state, and the pressure is in the "low" and "ok" states.
The pressure values ensure that only rules 2 and 3 fire:

## Slide 12: Defuzzification
It is the reverse process of fuzzification.
Defuzzification is the process of producing a quantifiable result in Crisp logic, given fuzzy sets and corresponding membership degrees. It is the process that maps a fuzzy set to a crisp set. It is typically needed in fuzzy control systems.

## Slide 13
There are 7 main methods
Max Membership Principle
Weight average Method
Mean Max Method
Centroid Method
Centre of Sum
Centre of largest Area
First Maxima (or) Last Maxima

## Slide 14: Max Membership Principle

## Slide 15: Weight average Method

## Slide 16: Mean Max Method

## Slide 17: Centroid Method Example : A1, A2 and A3 are three fuzzy sets as shown in below diagram

## Slide 23: Centre of Sum

## Slide 24: First Maxima (or) Last Maxima

## Slide 25: Fuzzy Arithmatic