## Slide 1
Lecture No:13
Topic: Power Flow Solution – Number of buses & Equations at each Bus
Course: Power System Analysis
Presented by
Dr M.S.Giridhar
Professor, Department of EEE
Lakireddy Bali Reddy College of Engineering (Autonomous)
Developed by
Jawaharlal Nehru Technological University Kakinada
www.jntuk.edu.in

## Slide 2: Unknown Quantities at each BUS
Active Power Injected at Bus-i Pi
Reactive Power Injected at Bus-i Qi
Voltage Magnitude at Bus-i |Vi|
Voltage Angle at Bus-i i
Each bus of the network has two such equations, and the power-flow problem is to solve Eqs.(1) and (2) for values of the unknown bus voltages which cause Eqs.(3) and (4) to be numerically satisfied at each bus.
Eqs.(3) & (4)
Solve
Check

## Slide 3: 4-Bus Power System Network
G1
G2
1
2
3
4
Slack Bus
PQ-Bus
PQ-Bus
PV-Bus

## Slide 4: Number of buses in power system network
Ng
Voltage controlled Buses (PV-Buses)
N-Ng-1
Load Buses (PQ-Buses)
N-Bus Power System Network
Slack Bus
(only ONE)

## Slide 5: Number of Equations in power system network
Ng
Voltage controlled Buses (PV-Buses)
2(N-Ng-1 )
Load Buses (PQ-Buses)
(2N-Ng-2) equations Power System Network
Slack Bus
(ZERO)

## Slide 6: Power Flow Solution
The unscheduled bus-voltage magnitudes and angles in the input data of the power-flow study, are called state variables or dependent variables since their values, which describe the state of the system, depend on the quantities specified at all the buses.
Hence, the power-flow problem is to determine values for all state variables by solving an equal number of power-flow equations based on the input data specifications .

## Slide 7: Gauss-Seidal Power Flow Solution-Mathematical Formulation