## Slide 1
Lecture No:30
Topic: Classification of Power System Stability
Course: Power System Analysis
Presented by
Dr M.S.Giridhar
Professor, Department of EEE
Lakireddy Bali Reddy College of Engineering (Autonomous)
Developed by
Jawaharlal Nehru Technological University Kakinada
www.jntuk.edu.in

## Slide 2: Single machine – Infinite Bus System
G
Synchronous Generator
Infinite Bus

## Slide 3: Elementary concepts of steady state, Dynamic and Transient Stabilities
Power System stability is classified into three basic types
Steady state stability
Dynamic stability
Transient stability

## Slide 4
Time (sec)
(t)
00
Ref.Axis
RotorAxis


## Slide 5: Steady state stability
The study of steady state stability is concerned with the determination of upper limit of the machine loading before losing synchronism, provided the loading is increased gradually.

## Slide 6: Dynamic stability
The system is said to be dynamically stable if the oscillations do not acquire more than certain amplitude and die out quickly (the system is well damped).
In a dynamically unstable system the oscillation magnitude is large and they persist for a long time (the system is undamped)
Dynamic stability study is carried out for 5-10 sec and some times upto 30 sec’s.

## Slide 7: Transient stability
For a large disturbance, changes in the angular differences are so large as to cause the machine to fall out of step, this type of stability is known as transient instability.
This fast phenomenon occurs with in 1 sec for a generator close to the cause of disturbance.